## Slide 1
H2020-MSCA-RISE-2015 ⎯ Grant Agreement N° 690835
Muse Collaboration Meeting,
October 23, 2018
Analysis of Local Monitor Signals
Nandita Raha, INFN Pisa

## Slide 2
Laser System - Basics
SM: Monitors the laser source.
x 6

## Slide 3: Old and New PMTs
Calorimeter | Old PMT | New PMT
11 | 25 | 5
12 | 26 | 0
13 | 27 | 6
18 | 28 | 8
20 | 29 | 4
Looking at calo 20 in detail – overall behaviour of all channels in back up. Since the amplitude is free from jitter of the pedestals, I used the amplitude instead of area for this presentation (though area plots are the same). Details of amplitude of first pulse here, as it will have the effect of temperature of the PMT alone.

## Slide 4: Parameter Definitions
Pedestal: Average first 50 samples
Amplitude: Pedestal subtracted peak sample
Area window: + 50 samples from peak.

## Slide 5: Comparison of old and new PMTs for Calo 20
Normalized area first pulse
Normalized area second pulse
Old PMTs about 1.5 times greater drop than new ones
Analysis based on 60 hour dataset

## Slide 6: Comparison of old and new PMTs for Calo 20
New PMT – Calo 20, channel 4
Old PMT – Calo 20, channel 29
Bin size = 50 mins.

## Slide 7: Temperature Variation – Channel 4
Note: Bottom plot clearly shows a negative temp coefficient
Laser hut temperature
Optical table temperature
Overlaid temperature and A1 on the same plot

## Slide 8: Temperature Variation – Channel 4
Overlaid temperature and A1, A2 and A2:A1 on the same plot, after normalizing all to A1 for consistency
Optical table temperature

## Slide 9: Amplitude Vs. Temp – Channel 4
A linear fit on the temperature Vs. amplitude plots – gives the approx. gain drop / oC

## Slide 10: Amplitude Vs. Temp – all channels
Amp 1
Amp 2
A2:A1
A linear fit on the temperature Vs. amplitude plots – gives the approx. gain drop / oC for every channel (or calorimeter)

## Slide 11: Comparing A1 and A2 – a special run 18413
Run 18413 – 24 hours
Normalized by the mean of first 5 bins
A2
A1
PMMA Channel 23
Silica Channel 24
A2
A1

## Slide 12: Conclusions
A1 primarily indicates the gain fluctuation of the PMT, as it is directly connected to the PMT from SM. As expected we have a negative correlation with temperature (PMT gain). A1 is similar for channels 23 and 24 does not depend on the type of fiber used.
A2 can have additional effects in fluctuation due to forward and reverse fibers to and from the calorimeters respectively.
  For silica no visible effects on A2.
  For PMMA "strange" and significant drop behind Gain variation – maybe attributed due to heating effect of temperature.
In any case LM correction is not necessary – the long term out of fill effects due to environmental factors do not effect the short term in fill SiPM gain function.

## Slide 13: Back Up Slides

## Slide 14: Temp dependence on A1 – Channel 23
Channel 23, Amplitude 1
Run 18413

## Slide 15: Checking all channels A1 and A2 overlaid – other run
PMMA Channel 23
Silica Channel 24
Channel 0
Channel 1

## Slide 16
Ratio of ratios for Calo 20
R = A2:A1 of new PMT and R’ = A’2:A’1 of old PMT. The ratio of these ratios R: R’ (new:old) is slightly unstable => The “return” component is not stable.
Fitted with p1 just to get a rough idea of the drop in ratio of ratio’s per min. This is 7e-7/min for calo 20

## Slide 17
Ratio of ratios other calos
Calo 11
Calo 12
Calo 13
Calo 18

## Slide 18
Variation Ratio of ratios/min
Mostly, the drop is of the order of ~10-7/min

## Slide 19: Recap - Temperature variation calo 20
Reminding the temp variations of A1, A2 and A2:A1 for channel 29 and 4– old PMT of calo 20.
Channel 29
Channel 4

## Slide 20: Temperature variation of Ratio of ratios- ch 20
This is to check the variation of any drift of the return signal from the calorimeters with temperature for this dataset.
Change is 0.16% / 0C

## Slide 21
Temperature Vs. Ratio of ratios other calos
Calo 11
Calo 12
Calo 13
Calo 18